## Slide 1
Analysis of total nitro compounds in water via batch reactor UV photolysis and colorimetric detection of nitrite
2024.11.14
Nguyen Cong-Hau, Valentin Rougé, Pham Thi Thai Ha Nguyen, Hyunjin Kim, Taekeun Son, and Yunho Lee*
*Email: yhlee42@gist.ac.kr
The 10th International Water Industry Conference (IWIC 2024)

## Slide 2: Contents
Formation of (halo) nitro compounds (NCs) in water.
Method optimization and development.
Applications:
Determining NC products from ozonation of amines/amino acids.
Occurence of NCs in river water and wastewater effluents.

## Slide 3
Formation of (halo) nitro compounds (NCs) in water
Algal blooms
Animals
Agriculture
Eutrophication
Sewage Discharge
Dissolved Organic Nitrogen
Water
Intake Sources
Nitrogenous DBPs
Protein
Fertilizer
Elements
Amino Acids
Humics
...
Disinfection/
Oxidation Treatment
Water Domestic Use
Known Substances
UnKnown Substances
Chloropicrin
1-nitropropane
Nitromethane
O3, UV/H2O2 or Cl2

## Slide 4
UV photolysis for quantifying total nitro(so) compounds
limited number of nitro compounds

## Slide 5
Research objectives
to develop total nitro compound (NC) quantification method based on batch reactor UV254 photolysis and colorimetric detection of nitrite;
to apply the method in water analysis and management.
Griess reagent
R–NO2
UV/vis
15,000 mJ/cm2
pH 12
SPE
(enrichment & removal of nitrite/nitrate)
Water sample
Flow of batch-reactor UV254 photolysis for total NC quantification in waters.

## Slide 6
Effect of UV fluence and pH on nitrite yield
nitromethane
https://www.sciencedirect.com/topics/chemistry/nitroalkane
similar Nitrite yield-UV dose dependence profile ( 10,000 mJ/cm2) for 2-nitroethanol, 1(2)-nitropropane, 2-bromo-2-nitropropane, and α-nitrotoluene.
Shi et al, ES&T, 2021 also reported enhanced UV light absorption in strongly alkaline condition. The molar extinction coefficient (pH 12) was shown as 2066 M-1cm-1.
pKa = 10.6
210
2319 M-1 cm-1 at 254 nm
Notes: nitromethane

## Slide 7
Nitrite yields from UV photolysis of NCs with different structures
0.01 M NaOH (pH 12)
15,000 mJ/cm2
Chloropicrin*: chlorinated products of nitromethane. Triplicate experiments.
15,000 mJ/cm2
68(17)%, n=8
57(27)%, n=10
19(23)%, n=6
11(11)%, n=5

## Slide 8
Conditioning
3.0 mL of MeOH
Loading
Wash
2.5 mL of ACN
Elution
3.0 mL of DIW
Flow rate: 10 mL/min
Sample volume: 1000 mL
Flow rate: 10 mL/min
Air flush: 5 min
50.0 mL of 1 mol/L NaCl
50.0 mL of DIW
Dry under gentle N2 (6 min)
Flow rate: 10 mL/min
Flow rate: 2 mL/min
Preconcentration procedure by solid phase extraction (SPE)
Batch UV photolysis
for total NC
2 mL ACN
8 mL H2O (NaOH)
10 mL
+
80-fold
sample enrichment

## Slide 9
Extraction efficiency during SPE for NCs
Selected NCs spiked in UW in the presence of NO2– + NO3 –
Selected NCs spiked in tap water
With SPE, LODs estimated as 2 nM (57% nitrite yield) for aliphatic NCs and 6 nM (19% nitrite yield) for aromatic NCs, with the overall enrichment factor of 80.
13%
%
200 nM

## Slide 10
NC products from ozonation of amines and amino acids
[PA]0 = 10 M, [O3]0 = 10 – 600 M
[t-BuOH] = 10 mM, pH 7 (5 mM PBS)
[O3]0/[PA]0
Ozonation of propylamine (PA)
60% as mol-NO2- per mol PA (total NC method)
O3
NO2–
UV254nm
61% NO2– yield
At [O3]0/[PA]0 = 10
indirect calculation from batch UV photolysis:
direct determination by LC/UV with standard: 97%
53% NO2– yield
NC yield = (53/61)*100 = 87%
From the pre-determined NO2– yield (53%) from UV photolysis of nitropropane, NC product yield (i.e., nitropropane) was calculated to be 87% (by batch UV photolysis). The calculated result was comparable to direct determination by LC/UV analysis (97%) using an authentic standard of nitropropane.
53% NO2– yield

## Slide 11
NC products from ozonation of amines and amino acids
Estimation approach for NC yields (%) using total NC method
Ref. 1:
26%
Ref. 2:
75%
Ref. 1: McCurry et al. (2016). Env Sci Tech, 50, 1209-1217 (O3 of 6-10 times target amines/amino acids).
Ref. 2: Shi & McCurry (2020). Env Sci Tech, 54, 2182-2191 (O3 of 10 times target amines/amino acids).
Ref. 1:
100%
Ref. 3:
60%
Ref. 3: Essaïed, K. A. et al. Water Research, 209, 117864. (O3 of 5 times target amines/amino acids).
[Amine]0 = 10 M, [O3]0 = 100 M
[t-BuOH] = 10 mM, pH 7 (5 mM PBS)
83(6)%, n=8
22(8)%, n=6
*
*When the standards for expected nitro products are unavailable, the average nitrite yield of 68% (0.68) for aliphatic NCs during batch UV photolysis method was used.
Notes: Yield of NC products (%) from ozonated amines and amino acids.
Nitrite yield of respective aliphatic NCs was used for calculating yield of NC products, except for (*), using average nitrite yield of aliphatic NC mixture.
Spiked 10 µM/each vs. 100 µM O3, 10 mM t-BuOH, and pH 7 (5 mM PBS).

## Slide 12
Occurance of total NCs in river water and wastewater effluents
g O3/g DOC
River water
Wastewater-1
Wastewater-2
g O3/g DOC
g O3/g DOC
Background NC concentration levels in river water and wastewater effluents.
Laboratory ozonation resulted in an increase in total NC concentrations  presence of NC precursors.
Complicated matrix components in wastewater can quench or consume added ozone ( 0.5 g O3/g DOC), compared to simple matrix of river water (total NC saturated 0.25 g O3/g DOC).
Total NC concentrations in laboratory ozonation of river water and wastewater effluents.

## Slide 13
Conclusions
This study successfully developed a novel analytical method to quantify total NC levels in waters, based on determining NO2– produced from batch reactor UV254nm photolysis (15,000 mJ/cm2) in a strongly alkaline solution (pH 12).
With SPE, the method showed good sensitivity: LOD 2 nM (aliphatic NCs) and 6 nM (aromatic NCs).
The method could be used to determine the NC product yields from ozonation of amines and amino acids: 83(6)% for 1/2 amines, and 22%(8)% for amino acids.
Application of the method to real water samples revealed the background NC in river water (88 nM) and in secondary effluent (138-180 nM). Ozonation can further increase total NC of up to 77 nM.
The developed methods can be useful for investigating the occurrence, fate, and transformation of nitro compounds in urban water cycle employing oxidative water treatment processes.
Future studies can focus on applications (more diverse water contexts, monitoring) and applying LC/MS-based methods to explain/identify the unknown portions.

## Slide 14
Thank you for your time and attention!
This study was supported by National Research Foundation of Korea (NRF, No. 2023R1A2C200616411).

## Slide 15
Yield of NC products from ozonation of amines and amino acids
[TCp]0 = 10 M, [O3]0 = 30 and 100 M
[t-BuOH] = 10 mM, pH 7 (5 mM PBS)
O3
UV
NO2–
1o/2o amines
NC products
nitrite
NO2– yield = X1
NO2– yield = X2
NC product yield = X1/X2
NO2– yield from the graph revealed the formation of NC products from ozonated amines and amino acids.
NC product formation depends on ozone doses.
TCp: target compound
Notes: Amines/amino acids  Ozonation  NCs  total NC method to determine yields of NC products as NO2– => reveal the formation potential of NCs from samples containing NC precursors.
Yields of NC products as NO2–: aliphatic amines > amino acids > aromatic amines.
It is clear that NC formation depends on ozone doses.