## Slide 1
Application of Optimized Analytical Assays Using Methylene Blue and Sodium Biphenyl for Quantifying Total PFASs in Water
Nguyen Cong-Hau1, Sangki Choi2, Heejong Son2, Yunho Lee1,*
1School of Earth Sciences and Environmental Engineering, Gwangju Institute of Science and Technology, Gwangju, Rep. of Korea
2Busan Water Quality Institute, 691 Dongbuk-ro, Sangdong-myun, Kimhae-si, Gyeongsangnam-do, Rep. of Korea
(*) E-mail: yhlee42@gist.ac.kr
The 13th IWA Micropol and Ecohazard Conference
Taipei, Taiwan, June 16-20, 2024

## Slide 2
The 13th IWA Micropol & Ecohazard Conference
Main Findings in this Study
MB Assay: A Semi-Quantification
02
Overall Analytical Method Performance
03
Contents
Sodium Biphenyl (SBP) Assay
01
Application to Simulated Water Samples
04
Application to Real PFAS-Containing Water
05
Defluorination Efficiency
TOP Assay to Improve the Selectivity

## Slide 3
PFAS as Contaminants of Emerging Concern
The 13th IWA Micropol & Ecohazard Conference
https://www.researchgate.net/publication/342976600_Fate_of_per-and_polyfluoroalkyl_substances_PFASs_modelling_source_identification_and_assessment_of_bioaccumulation_and_biodegradation
Per- and polyfluoroalkyl substances (PFAS, CnF2n+1−R).
Over 12,000 PFAS have been identified.
https://pfas-1.itrcweb.org
Potential Major Exposure Pathways of PFAS to Humans.
hydrophobic
hydrophilic
Considered as “anionic surfactants”
 mobile in water and environment.
Effects on the degradation in the environment.
H+
H+
Kwiatkowski, C. F. et al. Environ. Sci. Technol. Lett. 2020, 7 (8), 532–543.

## Slide 4
The 13th IWA Micropol & Ecohazard Conference
Needs to Develop Analytical Methods for Total PFAS
Overview of Different Analytical Approaches for PFAS and a Certain Concern of Unknown Portion.
Wang, Q. et al. (2023). TrAC Trends in Analytical Chemistry, 117351.
Adsorbable Organic Fluorine (AOF) Combustion-Ion Chromatography (CIC)
as a Standard Method for Unknown Organic F.
 PFAS adsorbed by activated carbon;
 Defluorination by combustion;
 Liberated fluoride is detected by IC.
TOP Assay
HPLC-(MS/)MS
Sophisticated instruments.
Limitation in selectivity for PFAS since CIC can include non-PFAS organofluorine.

## Slide 5
The 13th IWA Micropol & Ecohazard Conference
Needs to Develop Analytical Methods for Total PFAS
The MB assay
was adapted for smartphone-based methodsb;
includes non-PFAS anionic surfactants;
cannot capture the non-anionic PFAS precursors.
The SBP assay
was used in batch or flow injection analysis for some specific PFASa;
includes non-PFAS organofluorine.
Ion-pair reaction  extract to DCM;
UV/vis of DCM at 655 nm;
Chemical defluorination (compared to combustion defluorination in CIC);
Precolumn derivatization LC/UV for measuring the liberated F–.
Both methods still demonstrate a limitation in selectivity and sensitivity for PFAS.
Analytical Method Principle of Sodium Biphenyl (SBP) and Methylene Blue (MB) Assays.
aMusijowski, J. et al. Anal. Chim. Acta 2007, 600 (1-2 SPEC. ISS.), 147–154.
bAl Amin, M et al. Environ. Technol. Innov. 2020, 18, 100778.
Jones, B. C. et al. J. Pharm. Sci. 1971, 60 (7), 1036–1039.
Jurado, E. et al. Chemosphere 2006, 65 (2), 278–285.

## Slide 6
The 13th IWA Micropol & Ecohazard Conference
Persulfate Preoxidation (TOP Assay) to Improve the Selectivity
Conventional Role of TOP Assay:
Convert PFAS Precursors to Terminals to Estimate Precursor Contents by LC/MS.
Dora Chiang (2019)
The Entire Workflow for Quantifying Total PFAS in Water Using the Persulfate Preoxidation (TOP Assay) Followed by SBP or MB Assays.
TOP ASSAY IN THIS STUDY IS EXPECTED TO
decompose/oxidize the anionic surfactants (e.g., sodim dodecyl sulfate);
mineralize organofluorine into F–  washed out by the later SPE;
convert the non-anionic PFAS precursors to the anionic terminals  increase the inclusivity for MB assay.

## Slide 7
The 13th IWA Micropol & Ecohazard Conference
Research Objectives
This study developed an analytical method for total PFAS based on persulfate preoxidation, SPE, and chemical defluorination with SBP or ion-pair formation with MB.
The conditions of SBP and MB assays were optimized and tested for their responses with a range of PFAS structures, including PFAS terminals and precursors.
The effects of persulfate preoxidation and SPE on the selectivity and sensitivity of the methods were investigated using simulated samples spiked with various PFAS terminals and precursors, as well as other interferences such as organofluorine compounds, anionic surfactant, and F–.
The developed methods were applied to quantify total PFAS in industrial wastewater.
Reference methods: LC/MS (33 specific PFAS compounds*) and the CIC method to determine adsorbable organic fluorine (AOF).
*33 PFAS species: PFMOAA, PMPA, PFMOPrA, PFMOBA, PEPA, PFPrOPrA/HFPO-DA (“GenX”), ADONA, 9Cl-PF3ONS, 11Cl-PF3ONS, 4:2 FTS, 6:2 FTS, 8:2 FTS, PFBSA, PFHxSA, N-MeFOSAA, N-EtFOSAA, 6:2 diPAP, PFBA, PFPeA, PFHxA, PFHpA, PFOA, PFNA, PFDA, PFDoA, PFUdA, PFBS, PFPeS, PFHxS, PFHpS, PFOS, PFDS, and PFNS.

## Slide 8
The 13th IWA Micropol & Ecohazard Conference
Optimization of the SBP Assay for Total PFAS Analysis
1
The SBP Defluronation Efficiencies of Different PFAS Structures. Defluorinaiton efficiency (%) was calculated as CF-/(C0  NC-F)  100%, CF- is the molar concentration of F– released in the SBP assay, C0 is the initial molar concentration of each PFAS, and NC-F is the number of C-F bonds in the PFAS molecule.
(a)
(b)
Effects of TOP Assay on SBP Assay Responses of PFOA, Organofluorine and their Mixtures. fluocinolone acetonide-FCL, ciprofloxacin-CIP, 1-bromo-4-fluorobenzene-BFB.
C17H18FN3O3 5.7% F
C6H4BrF 10.9% F
C24H30F2O6 8.4% F

## Slide 9
The 13th IWA Micropol & Ecohazard Conference
Optimization of the MB Assay: A Semi-Quantification
2
Color Response of PFAS towards MB.
Persulfate Preoxidation (a) to Eliminate the Non-PFAS Surfactants and (b) to Convert PFAS Precursors into Anionic Terminals. 25 µg/L PFOA/PFOS and 80 µg/L SDS for (b) and 10 µg/L of each PFAS precursor for (a).
only PFOA used as a standard chemical
different color response among PFAS
different ion-pair formation levels between MB and anionic PFAS
MB: semi-quantification for total PFAS
SDS was effectively removed by persulfate preoxidation.
Non-anionic PFAS precursors originally showed negligible color response  persulfate preoxidation could convert them to anionic terminals  improve the inclusivity for the MB assay.
SDS (sodium dodecyl sulfate)
6:2 diPAP
non-anionic PFAS precursors

## Slide 10
The 13th IWA Micropol & Ecohazard Conference
Overall Analytical Method Performance
3
 | Sodium Biphenyl (SBP) | Methylene Blue (MB)
Limit of Detection | 0.016 µg F/L | 0.20 µg F/L
Precision Intra-day (RSDr) Inter-day (RSDR) | 1.8% 4.3% | 1.1% 4.5%
Recoveries | 85-100% | 101-133%
Analytical Performance for the Persulfate Preoxidation Followed by the SBP or MB Assays.

## Slide 11
The 13th IWA Micropol & Ecohazard Conference
Application to Simulated Water Samples
4
Selected PFAS were spiked to the sample matrix, i.e., PFPeA, PFHxA, PFHpA, PFOA, PFDA, PFHxS, and PFOS.
Total PFAS Concentrations (Expressed in µgF/L) of Simulated Water Samples, Presented as the Average Value  Standard Deviation for Triplicate Experiments.

## Slide 12
The 13th IWA Micropol & Ecohazard Conference
Application to Real PFAS-Containing Water Sample
5
Total PFAS Concentrations from Different Determination Procedures in Industrial Wastewater Effluent.
33 PFAS species: PFMOAA, PMPA, PFMOPrA, PFMOBA, PEPA, PFPrOPrA/HFPO-DA (“GenX”), ADONA, 9Cl-PF3ONS, 11Cl-PF3ONS, 4:2 FTS, 6:2 FTS, 8:2 FTS, PFBSA, PFHxSA, N-MeFOSAA, N-EtFOSAA, 6:2 diPAP, PFBA, PFPeA, PFHxA, PFHpA, PFOA, PFNA, PFDA, PFDoA, PFUdA, PFBS, PFPeS, PFHxS, PFHpS, PFOS, PFDS, and PFNS.
Total PFAS methods: higher results than target PFAS wTOP  indicating the presence of significant portions of unknown PFAS.
SBP and CIC woTOP: higher results than those wTOP  presence of organofluorine compounds (or adsorbable organic fluorine-AOF) other than PFAS.
SBP and CIC wTOP: comparable results  robustness of SBP assay.
MB assay wTOP: higher results than SBP & AOF wTOP  a breakdown of a single PFAS precursor into multiple anionic terminals (e.g., diPAP)  semi-quantification method.
targeted analysis
total quantification assays

## Slide 13
The 13th IWA Micropol & Ecohazard Conference
Conclusions
This study successfully developed a cost-effective analytical method for total PFAS quantification in waters using persulfate preoxidation (TOP assay) followed by SBP assay or MB assay.
The persulfate preoxidation strategy is integrated in the sample preparation to improve the method selectivity for PFAS, i.e., remove the anionic surfactants and organofluorine. The subsequent SPE can selectively preconcentrate PFAS & minimize/remove the impurities (sulphate, F–).
The SBP assay and reference CIC (wTOP) give comparable results, given that CIC is considered a more established method, indicating the robustness of the developed SBP assay.
The MB assay demonstrates its inherent limitation to give out higher concentrations, compared to the SBP assay as well as CIC (wTOP). However, with its simplicity, it is suggested to combine both of the SBP and MB assays, in which MB assay is used for initial screening purposes.
The developed assays should be applied to a wider range of different water scenarios. Besides the total PFAS concentration results, further advanced technique (e.g., high resolution mass spectrometry or HRMS) could be applied to identify unknown PFAS species.

## Slide 14
Thank you for your time and attention!
This study was supported by National Research Foundation of Korea funded by the Ministry of Science, ICT and Future Planning (NRF-2023R1A2C200616411).
The authors thank Seongbeom Jeon, Sujin Shin, Nguyen Pham Thai Ha, Eunji Lee, and Chaeyeong Park for the experimental support.

## Slide 15
CF-: molar concentration of F– (SBP assay);
C0: initial molar concentration of PFAS;
NC-F: number of C-F bonds.
Conditioning
3.0 mL of 0.1% v/v NH4OH in MeOH
Loading
Wash
3.0 mL of MeOH
Elution
3.0 mL of MeOH
3.0 mL of DIW
Dry under gentle nitrogen (6 min)
Flow rate: 10 mL/min
3.0 mL of 0.1% v/v NH4OH in MeOH
Dry under gentle nitrogen to dryness
Dissolve the residue by 1.00 mL of ACN
Sample volume: 300 mL
Flow rate: 10 mL/min
Air flush: 5 min
50.0 mL of 0.50% NH4OH (0.01%,)
50.0 mL of DIW
a mixed-mode, Weak Anion-eXchange, reversed-phase, water-wettable polymer
500 mg, 6 cc
Lee, Y. M. et al. (2020). Concentration and distribution of per-and polyfluoroalkyl substances (PFAS) in the Asan Lake area of South Korea. Journal of hazardous materials, 381, 120909.
Solid Phase Extraction (SPE) Procedure

## Slide 16
500 µL of PFAS or fluoride std
1.0 mL of 20% w/v SBP in diethyl ether
x
Vortex for 1 min
Let stand for 30 min
2.00 mL of DIW added
x
Vortex for 15 min
Discard the organic
x
Wash the aqueous once
Collect the aqueous phase for derivatization reaction with TPSiOH
1.00 mL of diethyl ether added
HPLC-DAD(UV) measurement
fluoride
organic chain
std: standard solution
DIW: deionized water
Defluorination Procedure between PFAS and SBP.
1
2
3
4
Defluorination Reaction by Sodium Biphenyl (SBP)

## Slide 17
The free fluoride obtained from the defluorination reactions by SBP was further derivatized with triphenyl silanol (TPSiOH) for the analysis on the HPLC-DAD.
Reaction scheme:
R3SiOH + H+ + F–  R3SiF + 2H2O, R = phenyl group
Optimized reaction conditions were applied.
15 mL
2.0 mL F– (*)
2.0 mL conc. HClO4
50 µL TPSiOH reagent
1.0 mL of heptane
Derivatization Reactions in a 15-mL Centrifuge Tube.
and is the total F concentration calculated based on the chemical structure of each PFAS and from the TOF assay, respectively.
Derivatization Reaction with Triphenyl Silanol (TPSiOH)

## Slide 18
Application to Real PFAS-Containing Water Sample
5
The concentrations of 33 specific PFAS in (a) industrial wastewater effluent (IW) and (b) river water (RW) samples analyzed by LC/MS, both without and with TOP (persulfate preoxidaiton). 33 PFAS are: PFMOAA, PMPA, PFMOPrA, PFMOBA, PEPA, PFPrOPrA/HFPO-DA (“GenX”), ADONA, 9Cl-PF3ONS, 11Cl-PF3ONS, 4:2 FTS, 6:2 FTS, 8:2 FTS, PFBSA, PFHxSA, N-MeFOSAA, N-EtFOSAA, 6:2 diPAP, PFBA, PFPeA, PFHxA, PFHpA, PFOA, PFNA, PFDA, PFDoA, PFUdA, PFBS, PFPeS, PFHxS, PFHpS, PFOS, PFDS, and PFNS

## Slide 19
Application to Real PFAS-Containing Water Sample
5
Concentrations determined by LC/MS, SBP, CIC, and MB assays, both without and with TOP for (a) IW and (b) RW samples. Only results with TOP are shown for the MB assay. All concentrations are expressed as gF/L.

## Slide 20
Application to Real PFAS-Containing Water Sample
5